## Slide 1
SMART INDIA HACKATHON 2026
•
Problem Statement ID – 26180
•
Problem Statement Title – A field-deployable AI-powered Smart Farming Assistant
•
Theme – Agriculture, FoodTech & Rural Development
•
PS Category – Hardware
•
Team ID – TH10-HW
•
Team Name – AEGIS
Autonomous Edge Guidance & Intelligent Surveillance
Notes: Team AEGIS, Team ID TH10-HW, problem statement 26180 from Qualcomm under Agriculture, FoodTech and Rural Development. Hardware category.

## Slide 2
AEGIS
TH10-HW
AEGIS
Autonomous Edge Guidance & Intelligent Surveillance
Proposed Solution / Approach
•
Two-pass field intelligence. An 800 mm quadcopter flies an autonomous survey grid at 20–30 m, then revisits only the flagged coordinates at 3–5 m for close-up confirmation.
•
Edge AI that works offline. Jetson Nano runs segmentation during flight and the field station builds the orthomosaic locally, so no step of the pipeline waits on connectivity.
•
Ground nodes explain the cause. LoRa soil-moisture, leaf-wetness, temperature and water-level readings fuse with imagery, so a stressed zone gets a reason and not just a colour.
•
Every alert is evidence-backed. Class, severity, confidence, evidence photo and an explicit “needs inspection” state, delivered by app, field display or SMS in the local language.
•
₹80,000 payload, not ₹6.67 lakh. A modular low-cost sensing stack does the field-scouting work of an imported DJI Mavic 3M.
AEGIS end-to-end workflow
Field polygon
→
Survey grid mission
→
Synced image + GPS capture
→
Onboard inference
↓
Hotspot map
→
Low-altitude revisit
→
Sensor fusion
→
Farmer advisory
Innovation and uniqueness
Two-pass autonomy
The survey finds where the problem is; the revisit decides what it is.
Offline by design
Models, map tiles and history live on the field station, not the cloud.
Evidence, not verdicts
Confidence, evidence photo and an honest “unknown” state on every alert.
Repeat-flight history
Same route, altitude and hour each week, so growth trends are comparable.
SMART INDIA HACKATHON 2026
2
Notes: AEGIS is a two-pass drone system. The survey pass finds where the field is abnormal, the low-altitude revisit confirms what it is, ground nodes explain why, and edge AI issues a confidence-scored advisory offline.

## Slide 3
AEGIS
TH10-HW
TECHNICAL APPROACH
Layer 1
Field sensing
2 × ESP32 + LoRa SX1276 nodes
SEN0308 capacitive soil moisture via ADS1115
SHT31 air temp / RH, DS18B20 soil temp
Leaf wetness, rain gauge, water level
Reflectance panel for repeatable flights
Layer 2
Aircraft
800 mm carbon quad, 15″ props, 6S 10 Ah
4 × Tarot 4008 330 KV, 40 A ESCs
Pixhawk + ArduPilot, M10 GPS, TFmini Plus
IMX219 nadir camera on damped mount
Jetson Nano 4 GB — MAVLink time-sync + TensorRT
Layer 3
Field edge station
OpenDroneMap orthomosaic and RGB indices
U-Net / YOLO11n aerial segmentation on tiles
Rasterio + GeoPandas pixel-to-GPS projection
Duplicate merge, 2 m severity grid, GeoJSON
Rule-based fusion of imagery and sensors
Layer 4
Farmer interface
MapLibre GL offline map with problem layers
Local-language advisory with evidence photo
Field display and SMS fallback via SIM7600
Mission history for week-on-week comparison
Inspection log closes the loop with ground truth
Components / technology stack
ArduPilot
Pixhawk
MAVLink / pymavlink
Jetson Nano
Python
PyTorch + Ultralytics
ONNX / TensorRT
OpenDroneMap
Rasterio / GeoPandas
MapLibre GL
ESP32 + LoRa
SQLite
Implementation process
01
Survey-grid mission verified in ArduPilot SITL: take off, grid, camera trigger, return home.
02
Time-synced capture writes image, GPS and attitude to one record; fast GeoJSON hotspot map.
03
Paddy imagery collected at our own altitudes across several fields and dates, then labelled.
04
Pretrained encoders fine-tuned, exported to ONNX and TensorRT, benchmarked on the Jetson.
05
Post-flight orthomosaic turned into stress, water and canopy-gap layers with evidence images.
06
Two-pass demo: hotspots generate a reviewed low-altitude mission that updates the advisory.
SMART INDIA HACKATHON 2026
3
Notes: Four layers: field sensing on LoRa nodes, the aircraft with Pixhawk and Jetson Nano, the field edge station running OpenDroneMap and the models, and the offline farmer interface. Six-week build order on the right.

## Slide 4
AEGIS
TH10-HW
FEASIBILITY AND VIABILITY
Feasibility
Pixhawk, Jetson Nano, ESP32 are already in hand — no unproven parts.
ArduPilot, OpenDroneMap and pretrained encoders are reused; only the integration is custom.
3.2–3.7 kg all-up weight, 18–25 min per battery, 4–8 acres per mapping flight.
Viability
₹76,000–₹83,000 for a complete prototype against ₹6.67 lakh for a DJI Mavic 3M.
Per-acre scouting through FPOs and cooperatives keeps the cost off the smallholder.
Modular upgrade path: NIR, thermal and RTK add on without redesigning the aircraft.
Practical implementation
One crop, one district first — paddy, where open Indian disease data already exists.
Runs fully offline; alerts arrive by app, field display or SMS.
Six-week build order ends in a live two-pass field demonstration.
Potential challenges and risks
Strategies for overcoming them
01
Lab-trained disease models collapse on real field imagery.
→
Train and test on our own camera and altitudes; split data by field and date to stop leakage.
02
A 5 mm insect is under one pixel at mapping altitude.
→
Detect canopy damage first, then confirm on the 3–5 m revisit or a close-up phone image.
03
Hotspot coordinates drift away from the real plants.
→
Shared clock, calibrated camera intrinsics, logged attitude and AGL, orthomosaic correction.
04
Jetson Nano cannot carry heavy models in flight.
→
Nano-scale networks at 640 px, FP16 TensorRT, sampled frames, active cooling; mosaics run on the ground.
05
Rural fields have no usable network for hours.
→
Imagery, models, map tiles and advisories stay local; sync and SMS fire when a network appears.
SMART INDIA HACKATHON 2026
4
Notes: Every flight-critical part is already owned or proven. The prototype costs about 80 thousand rupees against 6.67 lakh for a Mavic 3M. Five named risks with the mitigation we will actually implement.

## Slide 5
AEGIS
TH10-HW
IMPACT AND BENEFITS
Potential impact on the target audience
Farmers
Problems located before they spread, and spray or irrigation applied to the flagged zone instead of the whole field.
FPOs and cooperatives
One aircraft serves many members, with shared scouting reports and a season-long field record.
Agriculture officers
Field-level maps with dated evidence photos make advisories and scheme reporting verifiable.
Nation
Lower chemical and water use per acre, and earlier warning of drought, flood and heat damage.
Benefits of the solution
Economic
Targeted intervention cuts pesticide, fertiliser and pumping spend. Capital cost is about ₹80,000 against ₹6.67 lakh for an imported multispectral drone, so an FPO can own one outright.
Environmental
Chemicals reach only the zones that show damage, and irrigation is advised only where soil moisture and canopy temperature both justify it — less runoff, less groundwater drawn.
Social
Diagnostics reach farms with no connectivity, in the local language, with the photograph and confidence attached — so advice can be questioned and checked, not just obeyed.
The drone finds where the problem is, close-up vision determines what it is, ground sensors explain why it is happening, and edge AI recommends what to check next.
SMART INDIA HACKATHON 2026
5
Notes: Impact runs from the individual farmer up to national input use. Benefits split into economic, environmental and social, each tied to something the system actually measures.

## Slide 6
AEGIS
TH10-HW
RESEARCH AND REFERENCES
Field and applied research
•
Audited the low-cost NDVI imaging paper we were given: three printed NDVI equations are inverted and the system was never flown, so we use it only as a reflectance-calibration reference.
•
Scoped the prototype to paddy after checking which Indian crop has open, field-collected disease imagery and which problems are visible at 20–30 m.
Academic and technical sources
•
Development of an accurate low-cost NDVI imaging system for assessing plant health — Plant Methods, 2023. doi.org/10.1186/s13007-023-00981-8
•
Cucho-Padin et al. — Low-cost multisensor UAV for smallholder agriculture — NDVI agreement R² ≥ 0.8 and over 82% accuracy across 13 crop classes. link.springer.com/article/10.1007/s12518-019-00292-5
•
Mohanty et al. — Using deep learning for image-based plant disease detection — 99.35% on PlantVillage but about 31% on independent field images; the reason we train on our own data. frontiersin.org/articles/10.3389/fpls.2016.01419
•
Aasen et al. — Quantitative remote sensing with UAV spectral sensors — radiometric and geometric calibration practice for flight campaigns. mdpi.com/2072-4292/10/7/1091
•
Becker et al. — Separating nitrogen and water deficiency in maize — why nutrient and water stress cannot be told apart from one index. mdpi.com/2073-4395/10/11/1671
•
ArduPilot and QGroundControl survey-grid and camera-trigger documentation — mission geometry, overlap and geotagging workflow. ardupilot.org·docs.qgroundcontrol.com
Datasets and open source used for pretraining and reuse
Agriculture-Vision
Paddy Doctor
PlantDoc
IP102
OpenDroneMap
Fields2Cover
Ultralytics
Rasterio / GeoPandas
MapLibre GL
SMART INDIA HACKATHON 2026
6
Notes: We audited the NDVI paper we were given and found three printed equations inverted, which is why calibration is a reference and not a foundation. Datasets are reused for pretraining only; the field data is ours.